## Slide 1: Digital Circuit and System Lab09 AHB handshake
20250515
TA: 陳祖喬 Tsu-Chiao, Chen
Institute of Electronics,
National Yang Ming Chiao Tung University

## Slide 2: Environmental preparation
type ‘yes’ while you login the server
Extract files from TA’s directory (home directory)
  tar -xvf ~DCSTA01/Lab09.tar

## Slide 3: Flow Control: ready-valid flow
Ready 或valid 兩者都為1才能傳

## Slide 4: Handshake process
If(valid && ready)
Ready before valid / Valid before ready
Valid with ready

## Slide 5: AHB Interconnect
Basic components:
  Master
  Slave
  Arbiter
  Decoder
  Mux

## Slide 6: Lab - block diagram
Pattern
Master1 Master2 Master3 (done by TA)
Interconnect (inter.sv)
Slave memory 1
(done by TA)
Slave memory 2
(done by TA)

## Slide 7: Lab
Masters will send input data to interconnect
You should decode input data for valid, address and value
Based on master priority(1->2->3), send data to slave memory
Output handshake signal
[6:0] data_in_1 (from Master1)
data_in_1[6]: 0->slave1; 1->slave2
data_in_1[5:3]: address
data_in_1[2:0]: value
Ex: 7’b0101001 for slave1, addr=5, value=1
Ex: 7’b1011110 for slave2, addr=3, value=6

## Slide 8: inter.sv
Input Signal | Bit Width | Definition
clk | 1 | Clock
rst_n | 1 | Asynchronous active-low reset
in_valid_1 | 1 | in_valid from master1
in_valid_2 | 1 | in_valid from master2
in_valid_3 | 1 | in_valid from master3
data_in_1 | 7 | Data from master1
data_in_2 | 7 | Data from master2
data_in_3 | 7 | Data from master3
ready_slave1 | 1 | Ready signal from slave1
ready_slave2 | 1 | Ready signal from slave2

## Slide 9: inter.sv
Output Signal | Bit Width | Definition
valid_slave1 | 1 | valid signal to slave1
valid_slave2 | 1 | valid signal to slave2
addr_out | 3 | Address you want to write
value_out | 3 | Value you want to save
handshake_slave1 | 1 | High for 1 cycle after handshake with slave1
handshake_slave2 | 1 | High for 1 cycle after handshake with slave2

## Slide 10: Lab – FSM (ref.)
S_idle
S_master1
S_master2
S_handshake
In_valid_1=0 In_valid_2=1
In_valid_1=0 In_valid_2=0 In_valid_3=1
Valid&ready=1
Valid&ready=1
S_master3
Valid&ready=1
Wait next input
In_valid_1=1
Set valid high, wait ready
Set valid high, wait ready

## Slide 11: SPEC
Cycle time is fixed to 5.0.
It is an asynchronous reset and active-low architecture.
The reset signal (rst_n) would be given only once at the beginning of simulation. All output signals should be reset to 0 after the reset signal is asserted.
All output signals should be synchronized at positive edge of clock.
Handshake_slave signals should be pulled high in 30 cycle.
After handshake_slave signals is pulled high(only 1 cycle), pattern would check all value in slave memory, so master priority must be followed.
You are not allowed to modify syn.tcl.
After synthesis, the timing report should be non-negative (MET).
The synthesis result cannot include any latch and error.
Remember to check if a latch and error are synthesized (./08_check)
The gate-level simulation cannot include any timing violations.

## Slide 12: Waveform
negative trigger asynchronous reset

## Slide 13: Waveform
Input data

## Slide 14: Waveform
Master1 first
Decode: 0 110 101 => slave1 address:6 value:5

## Slide 15: Waveform
Set valid high, wait slave1 ready

## Slide 16: Waveform
Handshake!

## Slide 17: Waveform
output handshake signal

## Slide 18: Waveform
Continue for Master2

## Slide 19: Waveform
Pattern 1
Pattern 2

## Slide 20: Command List
Extract files from TA’s directory (home directory):
  tar -xvf ~DCSTA01/Lab09.tar
Verilog RTL simulation (01_RTL/):
  ./01_run_vcs_rtl
Synthesis (02_SYN/):
  ./01_run_dc_shell
  ./08_check
Gate level simulation (03_GATE/):
  ./01_run_vcs_gate
Observe waveform to debug
  nWave &
  find *.fsdb
  shift + L for reload fsdb file

## Slide 21: Score
Function Validity: 100%
  01_RTL PASS
  02_SYN timing slack must be MET, no error and latch
  03_GATE PASS, no error and timing violation
  You can not adjust your clock period by yourself, the clock period is 5 ns.
09_SUBMIT
  ./00_tar
  ./01_submit
  ./02_check 1st_demo/ 2nd_demo
Deadline :
  1st Demo: 5/15 18:20:00
  2nd Demo: 5/15 23:59:59